## Slide 1: Protection of surface waters through the State of Alaska on Alaska Refuges
Case study of Uganik River Reservation of Water within
Kodiak NWR
Notes: In this presentation we discuss the processing of the first water reservation adjudication between the state (DNR) and the USFSW.
We present
details about each agency and our policies,
details about the Uganik River and why it was selected for a water right and as the first adjudication,
and then we will discuss the process and the outcome.

## Slide 2: Statutory Mandates affecting Water Rights on Refuges
Alaska National Interest Lands Conservation Act (ANILCA) (1980)
  Primary purpose of each refuge in Alaska
    Conserve habitats in natural diversity
    Ensure “water quality and necessary water quantity”
National Wildlife Refuge System Improvement Act (NWRSIA) (1997)
  Maintain biological integrity/diversity/health
  Maintain adequate water quantity - quality
  Acquire water rights under State law

## Slide 3: Other Water & Law Factors on Alaska Refuges
Prior appropriation state w/ abundant water in unique hydrological and ecological systems
Progressive state water law
Expressed but unquantified FRWR in Alaska refuges
Sparse baseline hydrologic data
Limited ecological / biological data for aquatic habitat
Economic factors
  oil/gas development, placer mining, water export, fisheries/wildlife, recreation, navigation, etc.
Whole, intact, mostly pristine waters and watersheds, with water rights uncertainty
Notes: Assortment of thoughts in no particular order re Alaska and water rights. Unique, odd, peculiar, different characteristics and considerations related to instream water rights in Alaska
It is apart; does not abut another state; no possibility of interstate water dispute or need for compact or negotiation. (Some international trans-boundary issues being discussed in SE)
Lowest population density of any state (650,000 people) avg approx. 1 person/square mile vs lower 48 w/ 100 people/square mile
In contrast to most western, prior appropriation states, Alaska is not water deprived or over appropriated.
Relatively little out of stream appropriation

## Slide 4: Agency Mission Statements: Conflicts & Similarities
The U.S. Fish and Wildlife Service’s (FWS) mission is working with others to conserve, protect, and enhance fish, wildlife, plants, and their habitats for the continuing benefit of the American people.
The Alaska Department of Natural Resources’ (DNR) mission is to develop, conserve and maximize the use of Alaska’s natural resources consistent with the public interest.
Notes: Conserve for entities other than our agencies.

## Slide 5: Mission Statements: Conflicts & Similarities cont…
FWS
Conserve
Protect and enhance fish, wildlife, plants, and their habitats
for the benefit of the American people
DNR
Conserve and maximize
Develop the use of natural resource (lands and waters)
for public interest
Notes: FWS mission statement speaks to the fact that we are primarily a conservation agency.
Our mission is to protect and enhance fish and wildlife and their habitats noting that water is essential to this mission.
And it is all done for the benefit of the American people, including citizens of the State of Alaska

## Slide 6: Mission Statements: Conflicts & Similarities cont…
A Reservation of Water is the best route to gain protection and provide conservation….it is an opportunity.
The FWS aims to meet its legal obligations to protect the natural diversity of populations and habitats under ANILCA by working through the state. It is the appropriate first step in ensuring water quality and quantity for refuges.
Notes: It is an opportunity because
Of AK's progressive water
And the fact that the waters aren’t over appropriated.

## Slide 7: Agency’s Water Right Policy
FWS
Obtain sufficient water and water rights
Secure water rights under State law
Assert and protect Federal interests in water, as necessary
DNR
Assure state interests within water for the public
Neutral in determination of a reservation decision
Notes: It is the Service's policy to comply with State laws, regulations, and procedures in obtaining and protecting water rights, both for Service facilities and for trust fish and wildlife resources on lands not owned by the United States, except where application of State statutes and regulations does not permit Federal purposes to be achieved. Federal reserved water rights will be quantified and asserted when necessary to accomplish the primary purpose of the reservation.
Obtain: Sufficient quantities of water and the legal right to use that water to develop, use, and manage refuge lands and facilities, protect endangered species, and maintain instream flows.
Secure: All water rights needed for Service facilities and programs should be secured under State laws and procedures when available.
Assert: Assert when necessary to protect federal interests in water.
Review: Review and comment on notices for water right applications filed by others on or near refuges.
Identify: Identify and evaluate water rights on lands proposed for acquisition or disposal.

## Slide 8: Reservation of Water Purposes AS 46.15.145 (a)(1)
Protect fish and wildlife
    Habitat, propagation, and migration
Recreation
    Swimming, fishing, hunting, natural values, etc.
Navigation/Transportation
    Sufficient quantity for boats, floatplanes, etc.
Water quality
    Sanitary and water quality reasons

## Slide 9: Agency’s Water Right Process
FWS:
  Conserve fish and wildlife populations and habitats in their natural diversity (ANILCA)
  Ensure water quality and necessary water quantity within the refuge (ANILCA)
  Maintain the natural flow regime (natural hydrograph: magnitude, frequency, duration, time and rate of change)
  Protect flows for important life stages and channel form and function
DNR
  Reserved to the people for common use and is subject to appropriation and beneficial use…
    Adjudication process assures:
      water is allocated in a reasonable and consistent manner based in part by public interest criteria
      Determination of the validity and amounts of a water right.
        Including conflicting claims among competing applications.
Notes: The natural flow paradigm notes that “modifications of the natural flow regime dramatically affects both aquatic and riparian species and their habitat in streams and rivers worldwide” (Poff et al 1997)
ANILCA
(i) to conserve fish and wildlife populations and habitats in their natural diversity;
(ii) to fulfill the international fish and wildlife treaty obligations of the United States;
(iii) to provide the opportunity for continued subsistence uses by local residents; and
(iv) to ensure water quality and necessary water quantity within the refuge.

## Slide 10: Why the Uganik River?
First adjudication between DNR and FWS
Data rich area (27 years of flow data)
Strong fisheries component
Low/No conflict issues that may arise in other FWS applications
Straightforward
An excellent start point
Notes: Uganik River has 27 years of data associated with the USGS gage station 1951-1978), fish periodicity, and biologic data associated with refuge work

## Slide 11: Uganik River History & Importance
Provides migratory, spawning, and rearing habitat for sockeye, pink, chum, Coho and chinook salmon, steelhead, and Dolly Varden
The Uganik River drainage basin is considered a major rainbow trout area
The lower river is high use, key habitat for brown bear
The East Arm of Uganik Bay, into which the Uganik River flows, provides prime wintering habitat for puddle ducks and maintains a high concentration of waterfowl.
Subsistence hunting and trapping for residents of Port Lions and Ouzinkie
Notes: The Kodiak NWR was originally established to protect brown bear habitat, especially feeding and breeding habitat. Conservation of brown bear and their habitat is a purpose of Kodiak NWR under ANILCA.

## Slide 12
Notes: Point to Uganik Bay and the River drainage

## Slide 13
Notes: Note that there are no large tributaries entering the river in the reach that contribute at a point below the point of measurement.

## Slide 14: Uganik River
Notes: Looking upstream

## Slide 15: Uganik River Reservation Process
Review the annual hydrograph
Include the biologic aspect of the system in the form of fish life stage events
Consider periods of changing flow, duration of those events, and magnitude of those events
Define reservation time periods
Define volume of flow associated with each time period
Notes: Include both mean and median flow as well as each year’s hydrograph to show the variability of flow
The skewed mean (of this non normal or non-parametric variable) is not representative of the true monthly “normal” flow.
the median value for a period of flow gives a better representation of the central tendency or normal of the period
The median value for a period of flow is equivalent to the fifty percent exceedance probability (Q50) which is a statistically valid representation of normal flow.

## Slide 16
Notes: Include both mean and median flow as well as each year’s hydrograph to show the variability of flow
The skewed mean (of this non normal or non-parametric variable) is not representative of the true monthly “normal” flow.
the median value for a period of flow gives a better representation of the central tendency or normal of the period
The median value for a period of flow is equivalent to the fifty percent exceedance probability (Q50) which is a statistically valid representation of normal flow.

## Slide 17: Uganik River Reservation Timeline
Applied for on 9/27/2001
Adjudication process began January 31, 2012
Email and in face correspondence between DNR and USFWS March 20, 2012 – June 12, 2014.
Public/Agency notice published August 1, 2014
Certificates signed September 19, 2014
Recorded certificates received January 14, 2015

## Slide 18: Considerations in Flow Discussions
USFWS
  Fisheries/biological purpose
  Critical habitat needs
  Timing of flow events
  Overwintering
  Channel form and function
  River continuum paradigm
DNR
  Fisheries/biological purpose
  Critical habitat needs
  Timing of flow events
  Competing uses (prior/future)
  Unappropriated Flows
  Laws
  Public Resource

## Slide 19: Uganik Reservation Discussion
Time Period | Mean Time Discharge (cfs) | USFWS Requested Flow (cfs) | % Exceed | ADNR 1/2014 (cfs) | % Exceed | USFWS (cfs) | % Exceed | ADNR 4/3/2014 (cfs) | % Exceed | USFWS (cfs) | % Exceed | FWS alt 5/20/14 | % Exceed
January* | 232 | 250 | 18-20% | 150 | 45% | 230* | 25% | 150 | 45% | 200 | 32% | 200 | 32%
February* | 167 | 250 | 18% | 130 | 45% | 180* | 25% | 130 | 45% | 150 | 34% | 170 | 27%
March* | 150 | 250 | 10% | 125 | 45% | 150* | 25% | 125 | 45% | 140 | 35% | 147 | 28%
April 1-14 | 172 | 140 | 50% | 119 | 70% | 140 | 50% | 140 | 50% | 140 | 50% | 140 | 50%
April 15-30 | 274 | 245 | 50% | 175 | 70% | 245 | 50% | 245 | 50% | 245 | 50% | 245 | 50%
May 1-14 | 623 | 589 | 50% | 355 | 70-75% | 590 | 50% | 590 | 50% | 590 | 50% | 590 | 50%
May 15-31 | 1049 | 958 | 50% | 730 | 70-75% | 960 | 50% | 960 | 50% | 960 | 50% | 960 | 50%
June | 1770 | 1460 | 64% | 1280 | 75% | 1460 | 60-65% | 1460 | 60-65% | 1460 | 60-65% | 1460 | 60-65%
July | 1460 | 1160 | 62-63% | 990 | 75% | 1160 | 60-65% | 1160 | 60-65% | 1160 | 60-65% | 1160 | 60-65%
August | 896 | 690 | 55-56% | 559 | 70% | 690 | 55-60% | 690 | 55-60% | 690 | 55-60% | 690 | 55-60%
September | 832 | 600 | 50% | 416 | 70% | 600 | 45-50% | 600 | 45-50% | 600 | 45-50% | 600 | 45-50%
October | 675 | 400 | 56% | 318 | 70% | 400 | 55-60% | 400 | 55-60% | 400 | 55-60% | 400 | 55-60%
November | 503 | 275 | 54-55% | 198 | 70% | 338 | 45% | 338 | 45% | 338 | 45% | 338 | 45%
December | 258 | 250 | 35-36% | 120 | 70% | 200 | 45% | 200 | 45% | 200 | 45% | 200 | 45%
*Consents but acknowledges flows are insufficient to protect fish and wildlife habitat, migration, and propagation |  |  |  |  |  |  |  |  |  |  |  |  | 
Notes: Flow determination can only result with compromise and consideration of each agencies purposes and responsibilities to the public
FWS can always top file with the state or work to settle FRWR under our policy if the adjudicated flows to do meet the purposes of the refuge

## Slide 20: Certificated Flows
TIME PERIOD | Mean Time Period Discharge (cfs) | Original Flow Requests (cfs) | Granted Reservation Flows (cfs) | Reservation Flows (gpd) | Remaining Flows for Appropriation (cfs) | Remaining Flows for Appropriation (gpd)
January* | 232 | 250 | 200 | 129,254,400 | 32 | 20,680,704
February* | 167 | 250 | 150 | 96,940,800 | 17 | 10,986,624
March* | 150 | 250 | 140 | 90,478,080 | 10 | 6,462,720
April | 226 | 170 |  |  |  | 
April 1-14 | 172 |  | 140 | 90,478,080 | 32 | 20,680,704
April 15-30 | 274 |  | 245 | 158,336,640 | 29 | 18,741,888
May | 859 | 720 |  |  |  | 
May 1-14 | 623 |  | 590 | 381,300,480 | 33 | 21,326,976
May 15-31 | 1049 |  | 960 | 620,421,120 | 89 | 57,518,208
June | 1770 | 1460 | 1460 | 943,557,120 | 310 | 200,344,320
July | 1460 | 1160 | 1160 | 749,675,520 | 300 | 193,881,600
August | 896 | 690 | 690 | 445,927,680 | 206 | 133,132,032
September | 832 | 600 | 600 | 387,763,200 | 232 | 149,935,104
October | 675 | 400 | 400 | 258,508,800 | 275 | 177,724,800
November | 503 | 275 | 338 | 218,439,936 | 165 | 106,634,880
December | 258 | 250 | 200 | 129,254,400 | 58 | 37,483,776
*Consents but acknowledges flows are insufficient to protect fish and wildlife habitat, migration, and propagation
Notes: FWS can always top file with the state or work to settle FRWR under our policy if the adjudicated flows to do meet the purposes of the refuge

## Slide 21: DNR Criteria in Decision
A certificate of reservation can only be issued if the four criteria are met:
  Prior appropriators rights aren’t affected
  Need exists
  Unappropriated waters exist
  Public interest (AS 46.15.080 (b))

## Slide 22: Changed Perspectives
FWS
  An understanding for DNRs mission
  Better understanding of the state adjudication process
  Willingness to compromise within the limits of our mission goals
DNR
  Better understanding of FWS mission
  Willing to assist in the application process and applying for a reservation of water – 11 AAC 93.142(c)

## Slide 23: Changed Perspectives/Results
FWS
  Good working relationship with DNR
  Completion of Uganik adjudication
  Cooperative scheduling of future adjudications
DNR
  Working with the applicant
  Defendable decision document (legally/purpose based)
  Certificate of Protection
The Uganik River was fully within refuge lands with minimal chance of any development occurring, which gave DNR the opportunity to view this river slightly different than other rivers.

## Slide 24: Adjudication Results – Goals met?
Were there struggles between the two agencies? YES
  Response delays
  Unclear request/responses
  Additional projects/other work
Did the agencies come to an agreeable conclusion without elevation? YES
Were there lessons learned for the next FWS file adjudicated? YES
  Both agencies!

## Slide 25: Lessons Learned
Initiate a kick off meeting to discuss each parties concerns/desires and outline action plan-clear action plan will avoid future misunderstandings
Each party should set goals for the process by clarifying what issues in the application are the most important
Create a timeline associated with the action plan that is agreed to by both organizations-the timeline will provide an schedule and a projected date for finalization
Create a forum for open and transparent communication
While there is an understanding that certain documents need additional internal review, a quicker adjudication occurs when requested actions are carried out in a speedy manner
One single point of contact familiar with the application
Notes: Have monthly or bi-monthly meetings to keep the schedule and actions moving along;
Each party should agree to provide justification for their flow requirements and support them scientifically;
Use very clear language in all correspondence and in the application;
When a difficult issue is causing excessive calls and emails, have a meeting and clarify the Service’s and DNR’s concerns and point of view;

## Slide 26: The End!
Questions?
Cathy Flanagan
Hydrologist/Water Rights Specialist
US FWS
cathleen_flanagan@fws.gov
907-786-3903
Kim Sager
Water Reservation Specialist/ Adjudicator
AK DNR
kimberly.sager@alaska.gov
907-269-2033